## Slide 1: SMACH
SiMulation of human Activity and energy Consumption in the Home
Needs in terms of population synthesis

## Slide 2: Smach presentation
A multi-agent simulation platform that considers human activity and decisions as one of the main causative factors of energy consumption
A bottom-up, explicit approach
An interdisciplinary team in the fields of psychology, sociology, statistics, AI, building energy modeling
Building energy model
Simulation of activity and decisions
Electrical appliances
Electricity tariffs
Focus on the organisational level of human activity in the home : Individual and collective dynamics and interactions that lead to the emergence of an organisation of daily life in the household
Schumann M., Reynaud Q., Sabouret N., Sempé F., Charrier, B., Albouys, J., Haradji, Y., Inard, C., Multi-Agent based simulation of human activity for building and urban scale assessment of residential load curves and energy use, Building Simulation 2021, Bruges, Belgium

## Slide 3
Multi-Agent based simulation of human activity for building and urban scale assessment of residential load curves
shower
breakfast
cooking
do the dishes
household
individual
Provisional schedule of activity sequences from Time Use data (time-use diaries)
Provisional activities get distributions of frequencies, durations, preferred periods based on the individual’s profile
Action selection
Two consecutive days will be different: variability comes from the ABM itself
Modelling daily activities
Notes: Each individual => an intelligent agent with goals (based on their individual provisional schedule described above), knowledge (other agents’ activities, price of energy, etc.) and preferences (e.g., whether one’s preferred indoor temperature is based more on economic or personal comfort considerations).
Each agent has an individual decision module that will determine the actions that are actually performed. The action selection process uses priority levels that vary dynamically for each action, depending on the agent's knowledge, preferences and context.
Each activity is performed in a specific location inside or outside the building which determines building occupancy.

## Slide 4: From activity to energy use
Linking human activities to appliance use and energy consumption
Example of specific electricity uses

## Slide 5: Scaling up to the population level
Generation of a representative population sample, similar to a survey
Simulation of each household sequentially
Moussawel et al. Assessing the benefits of an agent-based approach for occupant behavior modeling in power demand simulation of dwelling stock, 2025, ECOS conference 2025
Notes: On peut donc faire des études à l’échelle client, comme à l’échelle segment ou remonter au portefeuille EDF ou au national
Un intérêt RTE Echelle France, mais également pour le réseau à échelle plus locale pour des besoins d’investissement

## Slide 6: Current population synthesis module
Ad-hoc module
Quick (1 minute for 5,000 households)
No simulation needed. Trips comes from raw ENTD/EMP data (simple distance matrix)
Old IPF like generation, difficult to maintain and update
This generation is unable to generate all characteristics
  We use a second generation for the « secondary » characteristics : mainly energy related characteristics (tariff, peak/off peak hours, heater type, reaction to an increase in prices, etc.)

## Slide 7: The complete SMACH Model
Statistical data (census, field-specific surveys, tariff distribution…)
Population generation
Population
Activity selection
Individual agent
Energy model
Appliances models
Building model
Simulated activity
Load curves
Household
Individual outputs
Inputs
Provisional schedules
Time Use Surveys
Inputs
Behavior & decisions
Activity and behavior model
Feedback from Building Energy Model
External information, incentives or constraints
Population output
Aggregation
Interactions between individuals

## Slide 8: Studies examples
« Classical » simulation = 1 year simulation with 5,000 households representative of metropolitan France
Validation of hypotheses on a modification of the peak/off-peak rate distribution (only households with a peak/off-peak tariff) => Impact on the aggregated load curve at the national (France) level.
Validation of a hypothesis of increased EV consumption during an extremely cold winter (winter simulations for 1,000 urban households in apartments).
Study on self-consumption in a neighborhood (100 houses within a given IRIS zone).
…

## Slide 9: Quantifying the impact of “eco-behaviors” for peak shaving: cooking
Results of the model on activity rates and cooking power demand (1000 households average)
morning peak
evening peak
00:00
04:00
08:00
12:00
16:00
20:00
22:00
02:00
06:00
10:00
14:00
18:00
24:00
PP
PP
PP
00:00
04:00
08:00
12:00
16:00
20:00
22:00
02:00
06:00
10:00
14:00
18:00
24:00
Displacement of the preferential periods (PP) of cooking tasks outside of peak hours, with a maximum shift of 45 minutes
 A diversity of behaviors (anticipate, postpone, maintain)

## Slide 10
Behavior
Energy
“Participatory simulation” ergonomics study with a dedicated interface to validate the representation of daily life and interactions in the household
Comparison of SMACH and statistical reference data for each activity, individual type and day type
(population of 100 households)
sleeping
cooking
cleaning
Nb of repetitions
% of individuals
Measured
Time (h)
SMACH
Example of Household A for Tuesdays
0
24
23
22
21
20
19
18
17
16
15
14
13
12
11
10
9
8
7
6
5
4
3
2
1
0
100
200
300
400
500
600
700
800
900
1000
1100
1200
Energy (Wh)
Data
SMACH
% of individuals
Comparison between simulated and measured average weekly load-curve day-by-day
Micro-scale (household)
Macro-scale (population)
Dynamics of aggregated load curves
March
Validation

## Slide 11: Parameter file
Selecting a population
  Existing file (pre-generated)
  Using SMACH’s population generator(s) (e.g., representative French population)
Selecting simulation parameters
  Start time / stop time
  Activating specific behavioral / technical modules (vacation, thermal model, phovoltaïc production, using HPC, etc.)
Selecting outputs
  Energy consumption, Temperatures, Water consumption, Activity, Vehicule use…
Selecting study parameters
  Forcing heating types, electricity tariffs, building characteristics, weather…
A YAML file for:

## Slide 12: Population file

## Slide 13: EQASIM population
+ income

## Slide 14: integration SMACH/EQASIM
SMACH households
  Family
    Individual
      Age, sex, PCS, …
    Household type(couple, family, etc.)
    Income
  Housing
    Type, area, etc.
    Geographial data
  Energy-related characteristics
    Tariff
    Heating type
    Domestic hot water type
    EV
    Building energy regulations
    …
Secondary generation to
Add domain-specific data
TUS data (daily life data)
Simulations

## Slide 15: discussion
Coupling TUS data (provisional schedule) with trips generated by EQASIM
Need for population generation at different geographic levels (country, region, department, municipality, IRIS), within an “acceptable” time frame
Shared database (size / accessability / …)
Trip variability
Link with ENTD data (individual scale /household scale)